## Slide 1
Powering A Mercury Bot

## Slide 2: Batteries The Energy Source of Champions!
Fact: every Mercury bot has been powered by batteries
Battery selection is of primary importance
  Strongly influences (-ed by) motor selection in single battery bots
Battery Selection Can Effect
  Computing platform
  Motor and servo performance
  Sensor performance

## Slide 3: A Few Things to Consider
Cost
Voltage
Required run time
Charging complexity
Capacity
Weight
The efficiency of electronics attached to the battery
The worst case!

## Slide 4: Power System Diagram

## Slide 5: Current Consumption: Electronics

## Slide 6: Current Consumption: Servos
Not generally specified
Analog servos usually require less current than digital when in motion
  Correspondingly lower performance
Rule of thumb: standard servo stall current ~1A
  More likely to stall than motors during testing
2 servos = 2A

## Slide 7: Current Consumption: Motors
A Typical Mercury Bot
  Weighs 15 lbs
  Expected to climb a 30° incline @ 1m/s2
  Has four 2.78” dia. wheels
  Moves at 1m/s
  Operates around 30 min between charging
BoE* per Motor Torque, Current @ 65% eff.
  80 oz-in, where stall torque 320 – 400 oz-in
  1.3 A

## Slide 8: Some Good Motors

## Slide 9: Total Current Consumption
A

## Slide 10: Battery Capacity
C Rate – Time to discharge cell to cut off voltage
  Units are
    1hr = 1C
    0.5hr = 2C
    5hr = 0.2C
Multiply by capacity to get amount of time a battery can supply a given current until discharged (around 1V for NiMH)
Example: 1000 mAh at 2C (30 minute discharge time):

## Slide 11: Battery Selection

## Slide 12: Battery Selection

## Slide 13: Battery Capacity
2C for 4600 mAh battery
  9.2A > 8.7A
  It’s good!

## Slide 14: References
All About Batteries
  https://learn.adafruit.com/all-about-batteries/
What is C-Rate
  https://batteryuniversity.com/learn/article/what_is_the_c_rate
How to Calculate Battery Run-time
  https://batteryuniversity.com/index.php/learn/article/bu_503_how_to_calculate_battery_runtime
A Guide to Understanding Battery Specifications
  http://web.mit.edu/evt/summary_battery_specifications.pdf
Drive Motor Sizing Tool
  https://www.robotshop.com/community/blog/show/drive-motor-sizing-tool